Steps For Demo 1

1. After Onos ENV is setup, compile ONOS with buck build onos command.
2. Bring up ONOS by using ok clean command.
3. Start CLI by using onos localhost command.
4. Activate Required appllications as given below,
    app activate org.onosproject.yang
    app activate org.onosproject.yangdemo
    app activate org.onosproject.yms
    app activate org.onosproject.config
    app activate org.onosproject.restconf
    app activate org.onosproject.protocols.restconfserver
5. Set the path of restconfConfig.json and run the curl command to switch the Restconf to use YangRuntime.
6. Pre-configure netconf configurations on the Device.
7. Place netconf-cfg.json in path (@$ONOS_ROOT/tools/test/configs/)
8. Send json to start the netconf connection with devices.
9. Send configurations via json.
10. Ping from RT1 to RT2.